12X4K NDI UHD PTZ Video Camera

User Manual

Version V1.0

（English）

# Content

Content	2

SAFETY GUIDES	3

PACKING LIST	4

QUICK START	4

PRODUCT HIGHLIGHTS.	5

CAMERA SPEC.	5

CAMERA INTERFACE.	7

CAMERA DIMENSION.	7

IR REMOTE CONTROLLER.	8

VISCA IN（RS232）PORT.	10

VISCA PROTOCOL	11

PELCO-d Protocol	21

PELCO-p protocol	22

osd menu	23

uvc control	24

wEB SETTING	27

View rtsp video via vlc	32

NEWTEK TOOLS guides……………………………………………………………………………………………………………………………………………………………..33

VISCA over IP	35

# SAFETY GUIDES

- Before operation, please fully read and follow all instructions in the manual. For your safety, always keep this manual with the camera.

- The camera power input range is 100-240VAC(50-60Hz),ensure the power supply input within this rate before powering on.

- The camera power voltage is 12VDC, rated currency is 2A. We suggest you use it with the original power supply adapter supplied by the factory.

- Please keep the power cable, video cable and control cable in a safe place. Protect all cables especially the connectors.

- Operational environment: 0℃-50℃, humidity less than 90%.To avoid any danger, do not put anything inside the camera, and keep away from the corrosive liquid.

- Avoid stress, vibration and damp during transportation, storage and installation.

- Do not detect the camera housing and cover. For any service, please contact authorized technicians.

- Video cable and control cable should be individually shielded, and cannot be substituted with other cables. Do not direct the camera lens towards strong light, such as the sun or the intensive light.

- Use a dry and soft cloth to clean the camera housing. Applied with neutral cleaning agent when there is need to clean. To avoid damage on the camera lens, never use strong or abrasive cleaning agents on the camera housing.

10.Do not move the camera by holding the camera head. To avoid mechanical trouble, do not rotate the camera head by hand. NEVER MOVE THE CAMERA MANUALLY WHEN IT IS WORKING.

11. Put the camera on fixed and smooth desk or platform, avoid leaned installation.

12. Power Supply Polarity (Drawing)

Note:

The video quality may be affected by the specific frequencies of electromagnetic field.

Never grasp the head of the camera, and never move the camera by hand when it is working, otherwise, mechanism maybe destroyed.

# Packing list

Check all bellow items when open the package:

Camera	1

Power Adapter	1

Power Cable	1

RS232 Control Cable	1

USB3.0 Cable	1

Remote Controller	1

User Manual	1

Double-sided Adhesive	1

QC certification	1

# QUICK START

- Check all cable connections before power on.

2. Dial Switch Setting (at the bottom of the camera):

| Dial Switch（ARM） |
| --- |
|  | SW-1 | SW-2 | Instruction |
| 1 | OFF | OFF | Updating mode |
| 2 | ON | OFF | Debugging mode |
| 3 | OFF | ON | Undefined |
| 4 | ON | ON | Working mode |

| Dial Switch （USB） |
| --- |
|  | SW-5 | SW-6 | Instruction |
| 1 | OFF | OFF | Undefined |
| 2 | ON | OFF | Working mode |
| 3 | OFF | ON | Updating mode |
| 4 | ON | ON | Undefined |

| Dial Switch |
| --- |
|  | SW-3 | SW-4 | Instruction |
| 1 | OFF | OFF | reserve |
| 2 | ON | OFF | reserve |
| 3 | OFF | ON | reserve |
| 4 | ON | ON | reserve |

# PRODUCT HIGHLIGHTS

- Adopts most advanced ISP, 1/2.5 inch 8.5MP sensor, providing 3840x2160 p30 Ultra HD video resolution

- 4K wide angle optical lens: 12x optical zoom and 2x digital zoom , with 72.5 degree field of view;

- 4K video over IP, H.264, H.265 encoding;

- Support NewTek NDI V4.0 video transmission and control;

- NDI|HX, HDMI, 3G-SDI, USB outputs, fit for different application, 4K video streaming over NDI|HX and HDMI optional.

- White Balance, Exposure, Focus, Iris can be adjusted automatically or manually.

- Support POE: one single CAT5/6 to get video, control and power supply;

- Special Focusing Algorithm: fast and precise focusing performance when zooming or moving,

- Smooth PTZ mechanical design, accurate pan tilt motor control;

- 128 presets supported; Exposure parameter and white balance parameter can be saved in presets (in manual mode)

- Standard Sony VISCA, IP VISCA, PELCO-P, PELCO-D control protocol; IP VISCA over both TCP and UDP.

- Daisy chain supported, max 7 cameras connected in VISCA protocol.

- Image flip function, support upside-down installation;

- Fast video format switch: less than 3 seconds

- Supported field upgrade for ISP, ARM, FPGA and USB

- USB3.0 port compatible with USB2.0 output.

- Support RS232/RS485/UVC control

- Standard UVC1.5 protocol, seamlessly compatible with major video conferencing software and platform

- OSD menu in English and Chinese supported. IP address, streaming resolution and size can be set in OSD menu.

TECHNICAL SPEC

| Video Format | HDMI (V1.4) | 3840*2160P30/25 1920*1080P60/50/30/25/59.94/29.97/24 1920*1080I60/50/59.94 1280*720P60/50/30/25/59.94/29.97 |
| --- | --- | --- |
|  | SDI | 1920*1080P60/50/30/25/59.94/29.97/24 1920*1080I60/50/59.94 1280*720P60/50/30/25/59.94/29.97 |
|  | USB | 1920*1080P60/50/30/25（USB3.0） 1280*720P60/50/30（USB3.0） 1280*720P25（USB3.0&USB2.0） 1024*576P30（USB3.0&USB2.0） 960*540P30（USB2.0） 640*360P30（USB2.0） 512*288P30（USB2.0） |
|  | IP | 3840*2160@1~30 / 1920*1080@1~30 （Main Stream） 1280*720@1~30 / 1027*576@1~30 / 640*360@1~30 （Sub stream） |
|  | NDI | 3840*2160@15~30, 1920*1080@15~30, 1280*720@15~30, 1027*576@15~30, 640*360@30 (low bandwidth mode) |
| Video Interface | HDMI（V1.4）,SDI, NDI¦HX,USB3.0, USB2.0 |
| Sensor | 1/2.5” 8.5MP CMOS sensor |
| Zoom | f 3.92～47.32mm(12X), F1.8- 2.8, View Angle: 72.5°(Far)-6.3°(Near) |
| Rotation Angle | Pan: -170° ~ +170°; Tilt: -30° ~ +90° |
| Rotation Speed | Pan: 0°~120°/s ; Tilt: 0°~80°/s |
| Preset: | Remote controller: 10; RS232: 128; Accuracy: 0.1° |
| Control Port | RS232, RS485, NDI¦HX (VISCA over IP), USB3.0(UVC1.5), USB2.0(UVC1.1) |
| Network Speed | 1000M |
| Video encode | H.264/H.265 |
| Bit Rate Control | Variable Bit Rate, Constant Bit Rate |
| Video Bit Rate | 1024Kbps~20480Kbps |
| Supported Protocol | TCP/IP, HTTP, RTSP, DHCP ,RTMP, Onvif(2.4), NDI(V4.0) Visca over IP(TCP&UDP), HTML5, Visca, Pelco P, Pelco D |
| POE | Supported |
| Daisy Chain | Support RS232 serial daisy chain |
| Minimum Lux | 0.1lux |
| White Balance | Auto/Indoor/Outdoor/Manual/Push/Sodium Lamp Auto/Sodium Lamp |
| Exposure | Auto/Manual/Bright/Shutter/Iris |
| Focus | Auto / Manual |
| Iris | Auto / Manual |
| Electric Shutter | Auto / Manual |
| Gamma | Supported |
| WDR | Supported |
| BLC | Supported |
| 2D Noise Reduction | Supported |
| 3D Noise Reduction | Supported |
| Anti Flicker | OFF/50Hz/60Hz |
| Pan Tilt Flip | Supported |
| Input Voltage | DC12V/POE(IEEE802.3af) |
| Dimension | 220mm×190mm×173mm |
| Net Weight | 1.5KG |

Note: when HDMI output 4K, no video output from SDI and USB port.

# CAMERA INTERFACE

| 1.Camera Lens 2.Camera Base 3.IR Receiver Panel 4.Power Indicator Light 5.Dial Switch | 6. Tripod Screw Hole 7. Installation Hole 8. RS232 control port (input) 9. RS232 control port(output) | 10. HDMI port 11.3G-SDI port 12, USB port 13, RJ45 port(IP&NDI) 14. DC12V plug |
| --- | --- | --- |

CAMERA DIMENSION(mm)

IR REMOTE CONTROLLER

POWER

Under normal working mode, short press POWER key, to enter standby mode;

Press it again, the camera will do self-configuration, then go back to HOME position.

It will go to preset position if power on model has been set before.

FREEZE （Not Supported）

Short press FREEZE key to freeze/ unfreeze the image.

IRT (IR Transfer/IR Pass)

Open / close the IR pass function. Once press the IRT key, the camera will receive and

Pass the IR remote control signal to the codec/terminal (via VISCA IN port).

SET 1~SET4 ADDRESS SETTING

Long press for 3seconds until the key light ON, to set camera address.

CAM1~CAM4（CAMERA SELECTING）

Short press to select the relative camera.

NUMBER KEY (1-9)

Set preset: long press (3 seconds) the number key to set preset.

Run preset: Short press the number key to run preset.

CLR PRE (CLEAR PRESET)

CLR PRE+ number key: to clear the relative preset.

Long press to clear all preset.

LEARN

Reserved, not available now.

FOCUS KEY ( ON THE LEFT)

Manual focus, only valid under manual focus model.

ZOOM KEY( ON THE RIGHT SIDE)

Set the zoom rate

NAVIGATE KEY: UP/DOWN/LEFT/RIGHT

Under working mode, use navigate key to set the pan tilt, and select menu when enter OSD.

OK /HOME KEY

Under working mode, short press OK to make the camera go back to HOME position; and confirm the selection when enter OSD.

AF: Auto Focus

MF: Manual Focus

RESET: Reset camera

MENU: Enter OSD menu

LEARN+LIMIT L key: Set the pan tilt left limit position.

LEARN+LIMIT R key: Set the pan tilt right limit position.

LEARN+LMT CLR key: Clear the limit position.

BLC OFF/ BLC ON：Not Available

BRIGHT-/BRIGHT+: Set image brightness, only valid under bright priority exposure mode.

Video Format Keys:

Long press 3 seconds to select different video format output.

Note:

Long press F3 to switch to 3840*2160P30 mode (HDMI)

Long press F4 to switch to 3840*2160P25 mode (HDMI)

# VISCA IN （RS232 PORT）

| No. | Function |  | VISCA IN | RS485 |
| --- | --- | --- | --- | --- |
| 1 | DTR |  | 1 |  |
| 2 | DSR |  | 2 |  |
| 3 | TXD |  | 3 |  |
| 4 | GND |  | 4 |  |
| 5 | RXD |  | 5 |  |
| 6 | A |  | 6 | A(+) |
| 7 | IR OUT |  | 7 | IR OUT |
| 8 | B |  | 8 | B(-) |

| VISCA IN &Mini DIN Connection |
| --- |
| Camera VISCA IN | Mini DIN |
| 1 | DTR | 1 | DSR |
| 2 | DSR | 2 | DTR |
| 3 | TXD | 5 | RXD |
| 4 | GND | 4 | GND |
| 5 | RXD | 3 | TXD |
| 6 | A(+) | 6 | NC |
| 7 | IR OUT | 7 | NC |
| 8 | B(-) | 8 | NC |

| VISCA IN & DB9 Connection |
| --- |
| Camera VISCA IN | Windows DB-9 |
| 1 | DTR | 6 | DSR |
| 2 | DSR | 4 | DTR |
| 3 | TXD | 2 | RXD |
| 4 | GND | 5 | GND |
| 5 | RXD | 3 | TXD |
| 6 | A(+) |  |  |
| 7 | IR OUT |  |  |
| 8 | B(-) |  |  |

VISCA Network Construction:

SERIAL PORT CONFIGURATION

| Parameter | Value | Parameter | Value |
| --- | --- | --- | --- |
| Baud rate | 2400/4800/9600/115200 | Stop Bit | 1bit |
| Start Bit | 1 bit | Check Bit | None |
| Date Bit | 8 bit |  |  |

VISCA PROTOCOL

Part1 Camera Return Command

| Ack/Completion Message |
| --- |
|  | Command Packet | Note |
| ACK | z0 41 FF | Returned when the command is accepted. |
| Completion | z0 51 FF | Returned when the command has been executed. |

z = camera adderss+8

| Error Messages |
| --- |
|  | Command Packet | Note |
| Syntax Error | z0 60 02 FF | Returned when the command format is different or when a command with illegal command parameters is accepted |
| Command Not Executable | z0 61 41 FF | Returned when a command cannot be executed due to current conditions. For example, when commands controlling the focus manually are received during auto focus. |

Part 2 Camera Control Command

| Command type | function | command |  |
| --- | --- | --- | --- |
| AddressSet | Broadcast | 88 30 01 FF | Address setting |
| IF_Clear | Broadcast | 88 01 00 01 FF | I/F Clear |
| CommandCancel |  | 8x 21 FF |  |
| CAM_Power | On | 8x 01 04 00 02 FF | Power ON/OFF |
|  | Off | 8x 01 04 00 03 FF |  |
| CAM_Zoom | Stop | 8x 01 04 07 00 FF |  |
|  | Tele(Standard) | 8x 01 04 07 02 FF |  |
|  | Wide(Standard) | 8x 01 04 07 03 FF |  |
|  | Tele(Variable) | 8x 01 04 07 2p FF | p = 0(low)~7(high) |
|  | Wide(Variable) | 8x 01 04 07 3p FF |  |
|  | Direct | 8x 01 04 47 0p 0q 0r 0s FF | pqrs: Zoom Position (0(wide) ~0x4000(tele)) |
|  | Direct with speed | 8x 0A 04 47 0t 0p 0q 0r 0s FF | t: spd 0~7 pqrs: Zoom Position (0(wide) ~0x4000(tele)) |
| CAM_DZoom | ON | 8x 01 04 06 02 FF |  |
|  | OFF | 8x 01 04 06 03 FF |  |
|  | Combine Mode | 81 01 04 36 00 FF | Combine with optical zoom control |
|  | Separate Mode | 81 01 04 36 01 FF | Separate with optical zoom control |
|  | Stop | 81 01 04 06 00 FF | Enable In separate mode |
|  | Tele (Variable) | 81 01 04 06 2p FF | Enable In separate mode |
|  | Wide (Variable) | 81 01 04 06 3p FF | Enable In separate mode |
|  | Direct | 81 01 04 46 0p 0q 0r 0s FF | Enable In separate mode |
| CAM_Focus | Stop | 8x 01 04 08 00 FF |  |
|  | Far(Standard) | 8x 01 04 08 02 FF |  |
|  | Near(Standard) | 8x 01 04 08 03 FF |  |
|  | Far (Variable) | 81 01 04 08 2p FF | p=0 (Low) to 7 (High) |
|  | Near (Variable) | 81 01 04 08 3p FF | p=0 (Low) to 7 (High) |
|  | Direct | 8x 01 04 48 0p 0q 0r 0s FF | pqrs: Focus Position |
|  | Auto Focus | 81 01 04 38 02 FF |  |
|  | Manual Focus | 81 01 04 38 03 FF |  |
|  | One Push AF | 8x 01 04 18 01 FF |  |
| CAM_ZoomFocus | Direct | 8x 01 04 47 0p 0q 0r 0s 0t 0u 0v 0w FF | pqrs: Zoom Position (0(wide)~ 0x4000(tele)) tuvw: Focus Position |
| CAM_WB | Auto | 8x 01 04 35 00 FF |  |
|  | Indoor | 8x 01 04 35 01 FF |  |
|  | Outdoor | 8x 01 04 35 02 FF |  |
|  | OnePush | 8x 01 04 35 03 FF |  |
|  | ATW | 8x 01 04 35 04 FF |  |
|  | Manual | 8x 01 04 35 05 FF |  |
|  | Sodium lamp | 8x 01 04 35 08 FF |  |
|  | fluorescent | 8x 01 04 35 09 FF |  |
|  | OnePush Trigger | 8x 01 04 10 05 FF |  |
| CAM_RGain | Reset | 8x 01 04 03 00 FF | Manual Control of R Gain |
|  | Up | 8x 01 04 03 02 FF |  |
|  | Down | 8x 01 04 03 03 FF |  |
|  | Direct | 8x 01 04 43 00 00 0p 0q FF | pq: R Gain (0~0xFF) |
| CAM_Bgain | Reset | 8x 01 04 04 00 FF | Manual Control of B Gain |
|  | Up | 8x 01 04 04 02 FF |  |
|  | Down | 8x 01 04 04 03 FF |  |
|  | Direct | 8x 01 04 44 00 00 0p 0q FF | pq: B Gain (0-0xFF) |
| CAM_AE | Full Auto | 81 01 04 39 00 FF | Automatic Exposure mode |
|  | Manual | 81 01 04 39 03 FF | Manual Control mode |
|  | Shutter Priority | 81 01 04 39 0A FF | Shutter Priority Automatic Exposure mode |
|  | Iris Priority | 81 01 04 39 0B FF | Iris Priority Automatic Exposure mode |
|  | Bright | 81 01 04 39 0D FF | Bright Mode (Manual control) |
| CAM_Shutter | Reset | 8x 01 04 0A 00 FF | Shutter Setting |
|  | Up | 8x 01 04 0A 02 FF |  |
|  | Down | 8x 01 04 0A 03 FF |  |
|  | Direct | 8x 01 04 4A 00 00 0p 0q FF | pq: Shutter Position (0~0x15) |
| CAM_Iris | Reset | 8x 01 04 0B 00 FF | Iris Setting(0~0xD) |
|  | Up | 8x 01 04 0B 02 FF |  |
|  | Down | 8x 01 04 0B 03 FF |  |
|  | Direct | 8x 01 04 4B 00 00 0p 0q FF | pq: Iris Position (0~ 0x11) |
| CAM_Gain | Reset | 8x 01 04 0C 00 FF | Gain Setting (0~0x0F) |
|  | Up | 8x 01 04 0C 02 FF |  |
|  | Down | 8x 01 04 0C 03 FF |  |
|  | Direct | 8x 01 04 0C 00 00 0p 0q FF | pq: Gain Positon (0~0x0E) |
| CAM_Bright | Reset | 8x 01 04 0D 00 FF | Bright Setting |
|  | Up | 8x 01 04 0D 02 FF |  |
|  | Down | 8x 01 04 0D 03 FF |  |
|  | Direct | 8x 01 04 4D 00 00 0p 0q FF | pq: Bright l Positon (0~0x1B) |
| CAM_WDR | On | 8x 01 04 3D 02 FF | Exposure Compensation ON/OFF |
|  | Off | 8x 01 04 3D 03 FF |  |
|  | Direct | 8x 01 04 D3 pq FF | pq: ExpComp Position (0~0x6) |
| CAM_BackLight(BLC) | On | 8x 01 04 33 02 FF | BackLight On |
|  | Off | 8x 01 04 33 03 FF | BackLight Off |
| CAM_Sharpness | Reset | 8x 01 04 02 00 FF | Aperture Control |
|  | Up | 8x 01 04 02 02 FF |  |
|  | Down | 8x 01 04 02 03 FF |  |
|  | Direct | 8x 01 04 42 00 00 0p 0q FF | pq: Aperture Gain (0~0x0F) |
| CAM_Memory(preset) | Reset | 8x 01 04 3F 00 pp FF | pp: Preset Number(=0 to 127) Corresponds to 0 to 9 on the Remote Commander |
|  | Set | 8x 01 04 3F 01 pp FF |  |
|  | Recall | 8x 01 04 3F 02 pp FF |  |
| CAM_LR_Reverse | On | 8x 01 04 61 02 FF | Image Flip Horizontal ON/OFF |
|  | Off | 8x 01 04 61 03 FF |  |
| CAM_PictureFlip | On | 8x 01 04 66 02 FF | Image Flip Vertical ON/OFF |
|  | Off | 8x 01 04 66 03 FF |  |
| CAM_RS485Ctl | On | 8x 01 06 A5 02 FF |  |
|  | Off | 8x 01 06 A5 03 FF |  |
| CAM_Saturation | Saturation | 8x 01 04 A1 00 00 0p 0q FF | pq :saturation level 0x00~0x0f |
| CAM_Contrast | Contrast | 8x 01 04 A2 00 00 0p 0q FF | pq :Contrast level 0x00~0x0f |
| CAM_SpeedByZoom | On | 8x 01 06 A0 02 FF |  |
|  | Off | 8x 01 06 A0 03 FF |  |
| CAM_PTSpeed | PT Speed | 8x 01 04 C1 00 00 0p 0q FF | pq :PT speed 0x05~0x18 |
| CAM_ZoomSpeed | Zoom Speed | 8x 01 04 D1 00 00 0p 0q FF | pq :Zoom speed 0x01~0x07 |
| CAM_ZoomDisplay | On | 8x 01 06 C2 02 FF |  |
|  | Off | 8x 01 06 C2 03 FF |  |
| CAM_IRaddress | IR address | 8x 01 06 D8 0p FF | p:IR address 1~4 |
| CAM_Gamma | Gamma set | 81 01 04 5B 0p FF | P:Gamma NO. (0~4) |
| CAM_2D Noise Reduction | Direct | 8x 01 04 A5 0p FF | (0~0x01) |
| CAM_3D Noise Reduction | Direct | 8x 01 04 53 0p FF | (0~0x05) |
| FLICK | 50HZ | 81 01 04 23 01 FF |  |
|  | 60HZ | 81 01 04 23 02 FF |  |
|  | OFF | 81 01 04 23 00 FF |  |
| VideoSystem Set(factory) |  | 8x 01 06 35 00 pp FF | pp: Video format 1080P60 0x00 1080P50 0x01 1080I60 0x02 1080I50 0x03 1080P30 0x 04 1080P25 0x05 720P60 0x 06 720P50 0x07 720P30 0x08 720P25 0x09 1080P5994 0x0E 1080I5994 0x0F 1080P2997 0x10 720P5994 0x13 720P2997 0x14 1080P24 0x11 1080P2398 0x12 4K@30 0x15 4K@25 0x16 |
| VideoSystem Set(Sony) |  | 81 01 04 24 72 0p 0q FF | pq: Video format 1080P60 0x2e 1080P50 0x2f 1080I60 0x01 1080I50 0x04 1080P30 0x06 1080P25 0x08 720P60 0x09 720P50 0x0c 720P30 0x0e 720P25 0x11 1080P5994 0x13 1080I5994 0x02 1080P2997 0x07 720P5994 0x0a 720P2997 0x0f 1080P24 0x2a 1080P2398 0x2b 4K@30 0x1D 4K@25 0x1E |
| CAM_IDWrite |  | 8x 01 04 22 0p 0q 0r 0s FF | pqrs: Camera ID (=0000 to FFFF) |
| DHCP control | DHCP off | 8x 01 04 AE 00 FF | DHCP off |
|  | DHCP on | 8x 01 04 AE 01 FF | DHCP on |
| IP address control | IP set | 8x 01 04 AB 0p 0q 0r 0s 0m 0n 0x 0y FF | Set ip to :pq.rs.mn.xy |
|  | Mask set | 8x 01 04 AC 0p 0q 0r 0s 0m 0n 0x 0y FF | Set mask to :pq.rs.mn.xy |
|  | Gateway set | 8x 01 04 AD 0p 0q 0r 0s 0m 0n 0x 0y FF | Set gateway to : pq.rs.mn.xy |
| Mainstream | resolution | 8x 01 04 C2 00 0p 0q 0r 0s 0m 0n 0x 0y FF | pqrs : Column(x size) mnxy: Line (y size) only support: 1920*1080 1280*720 3840*2160 1024*576 |
|  | rate | 8x 01 04 C2 01 0p 0q 0r 0s 0m 0n 0x 0y FF | pqrsmnxy: bitrate (1024~20480kbps) |
|  | Encode Mode | 8x 01 04 C2 02 0p 0q FF | Mode sel:0xpq 0x00:h264 0x01:h265 |
|  | Frame Rate | 8x 01 04 C2 03 0p 0q FF | Frame rate:0xpq (15~30) |
|  | IDR | 8x 01 04 C2 04 0p 0q FF | IDR Setting:0xpq (5~120) |
|  | StreamRateMode | 8x 01 04 C2 05 0p 0q FF | Contor mode:0xpq 0x00:CBR 0x01:VBR |
| Substream | resolution | 8x 01 04 C3 00 0p 0q 0r 0s 0m 0n 0x 0y FF | pqrs : Column(x size) mnxy: Line (y size) only support: 640*360 |
|  | rate | 8x 01 04 C3 01 0p 0q 0r 0s 0m 0n 0x 0y FF | pqrsmnxy: bitrate (1024~10240kbps) |
|  | Encode Mode | 8x 01 04 C3 02 0p 0q FF | Mode sel:0xpq 0x00:h264 0x01:h265 |
|  | Frame Rate | 8x 01 04 C3 03 0p 0q FF | Frame rate:0xpq (15~30) |
|  | IDR | 8x 01 04 C3 04 0p 0q FF | IDR Setting:0xpq (5~120) |
|  | StreamRateMode | 8x 01 04 C3 05 0p 0q FF | Contor mode:0xpq 0x00:CBR 0x01:VBR |
| Color adjust | Coloradjust OFF | 8x 01 04 B6 00 FF | Color adjust off |
|  | Color adjust ON | 8x 01 04 B6 01 FF | Color adjust on |
|  | brightness balance OFF | 8x 01 04 B7 00 FF | Keep Brightness |
|  | brightness balance ON | 8x 01 04 B7 01 FF | No keep Brightness |
|  | Flare red | 8x 01 04 B8 dat FF | Flare mode red value Default is 32 |
|  | Flare green | 8x 01 04 B9 dat FF | Flare mode green value Default is 32 |
|  | Flare green | 8x 01 04 BA dat FF | Flare mode blue value Default is 32 |
| SYS_Menu | Menu On | 8x 01 06 06 02 FF | Turn on the menu |
|  | Menu Off | 8x 01 06 06 03 FF | Turn off the menu |
|  | Menu Back | 8x 01 06 06 10 FF | Menu step back |
|  | Menu Ok | 8x 01 7E 01 02 00 01 FF | Menu ok |
| IR_Receive | On | 8x 01 06 08 02 FF | IR(remote commander)receive ON/OFF |
|  | Off | 8x 01 06 08 03 FF |  |
|  | On/Off | 8x 01 06 08 10 FF |  |
| Pan_tiltDrive | Up | 8x 01 06 01 VV WW 03 01 FF | VV: Pan speed 0x01 (low speed) to 0x18 (high speed) WW: Tilt speed 0x01 (low speed) to 0x14 (high speed) YYYY: Pan Position(TBD) ZZZZ: Tilt Position(TBD) |
|  | Down | 8x 01 06 01 VV WW 03 02 FF |  |
|  | Left | 8x 01 06 01 VV WW 01 03 FF |  |
|  | Right | 8x 01 06 01 VV WW 02 03 FF |  |
|  | Upleft | 8x 01 06 01 VV WW 01 01 FF |  |
|  | Upright | 8x 01 06 01 VV WW 02 01 FF |  |
|  | DownLeft | 8x 01 06 01 VV WW 01 02 FF |  |
|  | DownRight | 8x 01 06 01 VV WW 02 02 FF |  |
|  | Stop | 8x 01 06 01 VV WW 03 03 FF |  |
|  | AbsolutePosition | 8x 01 06 02 VV WW 0Y 0Y 0Y 0Y 0Z 0Z 0Z 0Z FF |  |
|  | RelativePosition | 8x 01 06 03 VV WW 0Y 0Y 0Y 0Y 0Z 0Z 0Z 0Z FF |  |
|  | Home | 8x 01 06 04 FF |  |
|  | Reset | 8x 01 06 05 FF |  |
| Pan-tiltLimitSet | Set | 8x 01 06 07 00 0W 0Y 0Y 0Y 0Y 0Z 0Z 0Z 0Z FF | W:1 UpRight 0:DownLeft YYYY: Pan Limit Position(TBD) ZZZZ: Tilt Limit Position(TBD) |
|  | Clear | 8x 01 06 07 01 0W 07 0F 0F 0F 07 0F 0F 0F FF |  |

Part 3 Camera Control Command

| Command type | command | return | note |
| --- | --- | --- | --- |
| CAM_PowerInq | 8x 09 04 00 FF | y0 50 02 FF | On |
|  |  | y0 50 03 FF | Off(Standby) |
| CAM_ZoomPosInq | 8x 09 04 47 FF | y0 50 0p 0q 0r 0s FF | pqrs: Zoom Position |
| CAM_DZoomOnOffInq | 8x 09 04 06 FF | y0 50 0p FF | p 2: ON 3: OFF |
| CAM_DZoomModeInq | 8x 09 04 36 FF | y0 50 0p FF | p 0:combination mode 1:separate mode |
| CAM_DZoomPosiInq | 8x 09 04 46 FF | y0 50 0p 0q 0r 0s FF | pqrs: Zoom Position |
| CAM_SpeedByZoomInq | 8x 09 06 A0 FF | y0 50 0p FF | p 2: ON 3: OFF |
| CAM_PTSpeedInq(IR) | 8x 09 04 C1 FF | y0 50 pp FF | pp: 0x05~0x18 |
| CAM_ZoomSpeedInq(IR) | 81 09 04 D1 FF | y0 50 0p FF | p:0x00~0x07 |
| CAM_FocusModeInq | 8x 09 04 38 FF | y0 50 02 FF | Auto Focus |
|  |  | y0 50 03 FF | Manual Focus |
| CAM_FocusPosInq | 8x 09 04 48 FF | y0 50 0p 0q 0r 0s FF | pqrs: Focus Position |
| CAM_2D_Inq | 8x 09 04 A5 FF | y0 50 03 FF | (0~0x01) p: 0: off 1: on |
| CAM_3D_Inq | 8x 09 04 53 FF | y0 50 03 FF | (0~0x05) p:0:off 1: auto 2~5: noise level |
| CAM_WBModeInq | 8x 09 04 35 FF | y0 50 00 FF | Auto |
|  |  | y0 50 01 FF | Indoor mode |
|  |  | y0 50 02 FF | Outdoor mode |
|  |  | y0 50 03 FF | OnePush mode |
|  |  | y0 50 04 FF | ATW |
|  |  | y0 50 05 FF | Manual |
| CAM_RGainInq | 8x 09 04 43 FF | y0 50 00 00 0p 0q FF | pq: R Gain |
| CAM_BGainInq | 8x 09 04 44 FF | y0 50 00 00 0p 0q FF | pq: B Gain |
| CAM_SaturationInq | 8x 09 04 A1 FF | y0 50 00 00 0p 0q FF | pq: saturation |
| CAM_ContrastInq | 8x 09 04 A2 FF | y0 50 00 00 0p 0q FF | pq: contrast |
| CAM_AEModeInq | 8x 09 04 39 FF | y0 50 00 FF | Full Auto |
|  |  | y0 50 03 FF | Manual |
|  |  | y0 50 0A FF | Shutter priority |
|  |  | y0 50 0B FF | Iris priority |
|  |  | y0 50 0D FF | Bright |
| CAM_FlickerModeInq | 8x 09 04 AA FF | y0 50 0p FF | p 0: OFF 1: 50HZ 2: 60HZ |
| CAM_ShutterPosInq | 8x 09 04 4A FF | y0 50 00 00 0p 0q FF | pq: Shutter Position |
| CAM_IrisPosInq | 8x 09 04 4B FF | y0 50 00 00 0p 0q FF | pq: Iris Position |
| CAM_GainPosiInq | 8x 09 04 4C FF | y0 50 00 00 0p 0q FF | pq: Gain Position |
| CAM_ BrightPosiInq | 8x 09 04 4D FF | y0 50 00 00 0p 0q FF | pq: Bright Position |
| CAM_WDRModeInq | 8x 09 04 3D FF | y0 50 02 FF | On |
|  |  | y0 50 03 FF | Off |
| CAM_WDRPosInq | 8x 09 04 D3 FF | y0 50 0p FF | p: WDR Position |
| CAM_ApertureInq | 8x 09 04 42 FF | y0 50 00 00 0p 0q FF | pq: Aperture Gain |
| CAM_PresetExistInq | 8x 09 04 3F pp FF | y0 50 0q FF | pp: Memory number q: 1=preset exist 0=preset not saved |
| SYS_MenuModeInq | 8x 09 06 06 FF | y0 50 02 FF | On |
|  |  | y0 50 03 FF | Off |
| CAM_LR_ReverseInq | 8x 09 04 61 FF | y0 50 02 FF | On |
|  |  | y0 50 03 FF | Off |
| CAM_PictureFlipInq | 8x 09 04 66 FF | y0 50 02 FF | On |
|  |  | y0 50 03 FF | Off |
| CAM_IDInq | 8x 09 04 22 FF | y0 50 0p 0q 0r 0s FF | pqrs: Camera ID |
| CAM_DHCPInq | 8x 09 04 AE FF | y0 50 pp FF |  |
| CAM_IPInq | 8x 09 04 AB FF | y0 50 0p 0p 0q 0q 0r 0r 0s 0s FF |  |
| CAM_MASKInq | 8x 09 04 AC FF | y0 50 0p 0p 0q 0q 0r 0r 0s 0s FF |  |
| CAM_GATEWAYInq | 8x 09 04 AD FF | y0 50 0p 0p 0q 0q 0r 0r 0s 0s FF |  |
| CAM_FlareModeInq | 8x 09 04 B6 FF | y0 50 pp FF |  |
| CAM_FlareBrightModeInq | 8x 09 04 B7 FF | y0 50 pp FF |  |
| CAM_FlareRed | 8x 09 04 B8 FF | y0 50 pp FF |  |
| CAM_FlareGreen | 8x 09 04 B9 FF | y0 50 pp FF |  |
| CAM_FlareBlue | 8x 09 04 BA FF | y0 50 pp FF |  |
| CAM_VersionInq | 8x 09 00 02 FF | y0 50 ab cd mn pq rs tu vw FF |  |
| VideoSystemInq(Telycam) | 8x 09 06 23 FF | y0 50 pp FF | pp: Video format |
| VideoSystemInq(Sony) | 8x 09 04 24 72 FF | y0 50 0p 0p FF | pp: Video format |
| IR_Transfer | 8x 09 06 1A FF | y0 50 02 FF | On |
|  |  | y0 50 03 FF | Off |
| IR_Receive | 8x 09 06 08 FF | y0 50 02 FF | On |
|  |  | y0 50 03 FF | Off |
| Pan-tiltMaxSpeedInq | 8x 09 06 11 FF | y0 50 ww zz FF | ww: PanMaxSpeed zz: Tilt Max Speed |
| Pan-tiltPosInq | 8x 09 06 12 FF | y0 50 0w 0w 0w 0w 0z 0z 0z 0z FF | wwww: PanPosition zzzz: Tilt Position |
| MainstreamResolutionInq | 8x 09 04 C2 00 FF | y0 50 0p 0q 0r 0s 0m 0n 0x 0y FF | pqrs : Column(x size) mnxy: Line (y size) only support: 1920*1080 ,1280*720, 3840*2160 ,1024*576 |
| MainstreamRateInq | 8x 09 04 C2 01 FF | y0 50 0p 0q 0r 0s 0m 0n 0x 0y FF | pqrsmnxy: bitrate (1024~20480) |
| MainEncodeModeInq | 8x 09 04 C2 02 FF | y0 50 pp FF | Mode sel:0xpp 0x00:h264 0x01: h265 |
| MainFrameRateInq | 8x 09 04 C2 03 FF | y0 50 pp FF | Frame rate:0xpp (15~30) |
| MainIDRInq | 8x 09 04 C2 04 FF | y0 50 pp FF | IDR Setting:0xpp (5~120) |
| MainStreamRateModeInq | 8x 09 04 C2 05 FF | y0 50 pp FF | Contor mode:0xpp 0x00:CBR 0x01:VBR |
| SubstreamResolutionInq | 8x 09 04 C3 00 FF | y0 50 0p 0q 0r 0s 0m 0n 0x 0y FF | pqrs : Column(x size) mnxy: Line (y size) only support: 640*360 |
| SubstreamRateInq | 8x 09 04 C3 01 FF | y0 50 0p 0q 0r 0s 0m 0n 0x 0y FF | pqrsmnxy: bitrate (1024~20480 kbps) |
| SubEncodeModeInq | 8x 09 04 C3 02 FF | y0 50 pp FF | Mode sel:0xpp 0x00:h264 0x01: h265 |
| SubFrameRateInq | 8x 09 04 C3 03 FF | y0 50 pp FF | Frame rate:0xpp (15~30) |
| SubIDRInq | 8x 09 04 C3 04 FF | y0 50 pp FF | IDR Setting:0xpp (5~120) |
| SubStreamRateModeInq | 8x 09 04 C3 05 FF | y0 50 pp FF | Contor mode:0xpp 0x00:CBR 0x01:VBR |

Note:【x】 means the camera address ;【y】=【x + 8】.

VISCA Pan Tilt Absolute Position Value

| Pan Angle | VISCA Value | Tilt Angle | VISCA Value |
| --- | --- | --- | --- |
| -170 | 0xF670 | -30 | 0xFE50 |
| -135 | 0xF868 | 0 | 0x0000 |
| -90 | 0xFAF0 | 30 | 0x01B0 |
| -45 | 0xFD78 | 60 | 0x0360 |
| 0 | 0x0000 | 90 | 0x510 |
| 45 | 0x0288 |  |  |
| 90 | 0x0510 |  |  |
| 135 | 0x0798 |  |  |
| 170 | 0x0990 |  |  |

VISCA Pan Tilt Speed Value

| Pan(Degree/Second) | Pan(Degree/Second)) |
| --- | --- |
| 0 | 0.3 | 0 | 0.3 |
| 1 | 1 | 1 | 1 |
| 2 | 1.5 | 2 | 1.5 |
| 3 | 2.2 | 3 | 2.2 |
| 4 | 2.4 | 4 | 3.6 |
| 5 | 2.6 | 5 | 4.7 |
| 6 | 2.8 | 6 | 6 |
| 7 | 3.0 | 7 | 8 |
| 8 | 3.2 | 8 | 10 |
| 9 | 3.4 | 9 | 12 |
| 10 | 3.8 | 10 | 15 |
| 11 | 4.5 | 11 | 18 |
| 12 | 6 | 12 | 23 |
| 13 | 9 | 13 | 30 |
| 14 | 15 | 14 | 39 |
| 15 | 19 | 15 | 48 |
| 16 | 25 | 16 | 59 |
| 17 | 32 | 17 | 69 |
| 18 | 38 | 18 | 80 |
| 19 | 45 |  |  |
| 20 | 58 |  |  |
| 21 | 75 |  |  |
| 22 | 88 |  |  |
| 23 | 105 |  |  |
| 24 | 120 |  |  |

# PELCO-D PROTOCOL

| Function | Byte1 | Byte2 | Byte3 | Byte4 | Byte5 | Byte6 | Byte7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Up | 0xFF | Address | 0x00 | 0x08 | Pan Speed | Tilt Speed | SUM |
| Down | 0xFF | Address | 0x00 | 0x10 | Pan Speed | Tilt Speed | SUM |
| Left | 0xFF | Address | 0x00 | 0x04 | Pan Speed | Tilt Speed | SUM |
| Right | 0xFF | Address | 0x00 | 0x02 | Pan Speed | Tilt Speed | SUM |
| Upleft | 0xFF | Address | 0x00 | 0x0C | Pan Speed | Tilt Speed | SUM |
| Upright | 0xFF | Address | 0x00 | 0x0A | Pan Speed | Tilt Speed | SUM |
| DownLeft | 0xFF | Address | 0x00 | 0x14 | Pan Speed | Tilt Speed | SUM |
| DownRight | 0xFF | Address | 0x00 | 0x12 | Pan Speed | Tilt Speed | SUM |
| Zoom In | 0xFF | Address | 0x00 | 0x20 | 0x00 | 0x00 | SUM |
| Zoom Out | 0xFF | Address | 0x00 | 0x40 | 0x00 | 0x00 | SUM |
| Focus Far | 0xFF | Address | 0x00 | 0x80 | 0x00 | 0x00 | SUM |
| Focus Near | 0xFF | Address | 0x01 | 0x00 | 0x00 | 0x00 | SUM |
| Set Preset | 0xFF | Address | 0x00 | 0x03 | 0x00 | Preset ID | SUM |
| Stop | 0xFF | Address | 0x00 | 0x00 | Pan Speed | Tilt Speed | SUM |
| Clear Preset | 0Xff | Address | 0x00 | 0x05 | 0x00 | Preset ID | SUM |
| Call Preset | 0Xff | Address | 0x00 | 0x07 | 0x00 | Preset ID | SUM |
| Query Pan Position | 0Xff | Address | 0x00 | 0x51 | 0x00 | 0x00 | SUM |
| Query Pan Position Response | 0Xff | Address | 0x00 | 0x59 | Value High Byte | Value Low Byte | SUM |
| Query Tilt Position | 0Xff | Address | 0x00 | 0x53 | 0x00 | 0x00 | SUM |
| Query Tilt Position Response | 0Xff | Address | 0x00 | 0x5B | Value High Byte | Value Low Byte | SUM |
| Query Zoom Position | 0Xff | Address | 0x00 | 0x55 | 0x00 | 0x00 | SUM |
| Query Zoom Position Response | 0Xff | Address | 0x00 | 0x5D | Value High Byte | Value Low Byte | SUM |

# PELCO-P PROTOCOL

| Function | Byte1 | Byte2 | Byte3 | Byte4 | Byte5 | Byte6 | Byte7 | Byte8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Up | 0Xa0 | Address | 0x00 | 0x08 | Pan Speed | Tilt Speed | 0Xaf | XOR |
| Down | 0Xa0 | Address | 0x00 | 0x10 | Pan Speed | Tilt Speed | 0Xaf | XOR |
| Left | 0Xa0 | Address | 0x00 | 0x04 | Pan Speed | Tilt Speed | 0Xaf | XOR |
| Right | 0Xa0 | Address | 0x00 | 0x02 | Pan Speed | Tilt Speed | 0Xaf | XOR |
| UpLeft | 0Xa0 | Address | 0x00 | 0x0C | Pan Speed | Tilt Speed | 0Xaf | XOR |
| UpRight | 0Xa0 | Address | 0x00 | 0x0A | Pan Speed | Tilt Speed | 0Xaf | XOR |
| DownLeft | 0Xa0 | Address | 0x00 | 0x14 | Pan Speed | Tilt Speed | 0Xaf | XOR |
| DownRight | 0Xa0 | Address | 0x00 | 0x12 | Pan Speed | Tilt Speed | 0Xaf | XOR |
| Zoom In | 0Xa0 | Address | 0x00 | 0x20 | 0x00 | 0x00 | 0Xaf | XOR |
| Zoom Out | 0Xa0 | Address | 0x00 | 0x40 | 0x00 | 0x00 | 0Xaf | XOR |
| Focus Far | 0Xa0 | Address | 0x00 | 0x80 | 0x00 | 0x00 | 0Xaf | XOR |
| Focus Near | 0Xa0 | Address | 0x01 | 0x00 | 0x00 | 0x00 | 0Xaf | XOR |
| Stop | 0Xa0 | Address | 0x00 | 0x00 | Pan Speed | Tilt Speed | 0Xaf | XOR |
| Set Preset | 0xA0 | Address | 0x00 | 0x03 | 0x00 | Preset ID | 0xAF | XOR |
| Clear Preset | 0xA0 | Address | 0x00 | 0x05 | 0x00 | Preset ID | 0xAF | XOR |
| Call Preset | 0xA0 | Address | 0x00 | 0x07 | 0x00 | Preset ID | 0xAF | XOR |
| Query Pan Position | 0xA0 | Address | 0x00 | 0x51 | 0x00 | 0x00 | 0xAF | XOR |
| Query Pan Position Response | 0xA0 | Address | 0x00 | 0x59 | Value High Byte | Value Low Byte | 0xAF | XOR |
| Query Tilt Position | 0xA0 | Address | 0x00 | 0x53 | 0x00 | 0x00 | 0xAF | XOR |
| Query Tilt Position Response | 0xA0 | Address | 0x00 | 0x5B | Value High Byte | Value Low Byte | 0xAF | XOR |
| Query Zoom Position | 0xA0 | Address | 0x00 | 0x55 | 0x00 | 0x00 | 0xAF | XOR |
| Query Zoom Position Response | 0xA0 | Address | 0x00 | 0x5D | Value High Byte | Value Low Byte | 0xAF | XOR |

OSD MENU

1. Under working mode, press the MENU key on the IR remote controller, to enter the OSD menu as bellow:

2, After enter the main menu, use the navigate UP/DOWN key to select the main menu. Once been selected, the main menu will change to blue background, and the right side will show all sub menu options.

3, Press the navigate RIGHT key to enter sub menu; use UP/DOWN key to select the sub menu; use LEFT/RIGHT   key to select parameter.

4, Press the MENU key again to return to previous menu. Press the MENU key continuously to exit the OSD menu. Before exiting, will show up a window to select whether need to save all settings (use LEFT/RIGHT key to set). As bellow:

5. OSD Menu Setting List

| SYSTEM | PROTOCOL | VISCA,PELCO-P,PELCO-D | Default：VISCA |
| --- | --- | --- | --- |
|  | ADDRESS | VISCA:1~7 PELCO-P/D:1~255 | Default：1 |
|  | BAUD RATE | 2400,4800,9600,115200 | Default：9600 |
|  | PTL LOCK | Protocol lock: once set, above protocol setting will be locked | Default：OFF |
|  | RS485 | RS485 ON/OFF | Default：OFF |
|  | VISCA | To select VISCA sources Optional from via COM and via IP（VISCA over IP） | Default： OVER ALL |
|  | LANGUAGE | Chinese, English | Default：English |

| EXPOSURE | EXPOSURE MODE | AUTO,MANUAL,BRIGHT,SHUTTER,IRIS | Default：AUTO |
| --- | --- | --- | --- |
|  | SHUTTER | Shutter speed:1/8~1/10000, only valid under manual mode | Default：AUTO |
|  | IRIS | Iris setting:CLOSE~F1.5, only valid under manual mode | Default：AUTO |
|  | GAIN | Gain setting:0dB~28dB , only valid under manual mode | Default：AUTO |
|  | BRIGHT | Bright setting:0~15, only valid under bright priority mode. | Default：8 |
|  | WDR | ON/OFF | Default：OFF |
|  | WDR Level | WDR Level | Default：1 |
|  | BLC | ON/OFF | Default：OFF |

| IMAGE | WB MODE | AUTO,INDOOR,OUTDOOR,MANUAL,PUSH,SODIUM LAMP AUTO, SODIUM LAMP | Default：ATW |
| --- | --- | --- | --- |
|  | R GAIN | Red gain level: 0~255, only valid under manual white balance mode. | Default：AUTO |
|  | B GAIN | Blue gain level:0~255 , only valid under manual white balance mode | Default：AUTO |
|  | FLICK | Anti-Flicker setting:50/60HZ, to reduce the video flicker | Default：50HZ |
|  | DZOOM | Turn on/off digital zoom (2x digital zoome) | Default：OFF |
|  | FOCUS | Select focus mode | Default：AUTO |

| QUALITY | 2D NR | 2D noise reduction: the bigger value, the less noise on image, the lower resolution | Default：OFF |
| --- | --- | --- | --- |
|  | 3D NR | 3D noise reduction:OFF/AUTO/0~4, the bigger value, the less motion noise on image, high value will cause image smear. | Default：AUTO |
|  | SHARPNESS | Sharpness setting: 0~15, the higher value, edge of the image will be sharpen | Default：AUTO |
|  | CONTRAST | Set contrast level | Default：50HZ |
|  | SATURATION | Set saturation. | Default：8 |
|  | GAMMA | Select gammar level | Default：0 |
|  | AF SENSITIVITY | Optional：LOW/NORMAL/HIGH | Default:NORMAL |

| PTZ | SPEEDBYZ | SpeedByZoom: proportional speed, the bigger zoom, the slowerspeed | Default：ON |
| --- | --- | --- | --- |
|  | FLIP.HOR | Flip horizontal | Default：OFF |
|  | FLIP VER | Flip vertical | Default：OFF |
|  | PT SPD | Pan Tilt speed | Default：18 |
|  | ZOOM SPD | Zoom speed | Default：5 |
|  | MENU MIR | Turn on/off left/menu mirror function. | Default:NORMAL |
| FORMAT | 3840*2160P30 | 720P50 | Once selected, press OK key to confirm, if it is the selected video format, there is no change. 4K mode does not support menu switching, when switch to 4K model, menu will be existed automatically. |
|  | 3840*2160P25 | 720P29.97 |  |
|  | 1080P59.94 | 720P25 |  |
|  | 1080P50 | 1080P60 |  |
|  | 1080I59.94 | 1080P30 |  |
|  | 1080I50 | 720P60 |  |
|  | 1080P29.97 | 720P30 |  |
|  | 1080P25 | 1080I60 |  |
|  | 720P59.94 | 1080P24 |  |

| IP | DHCP | ON/OFF | Using up/down/left/right navigation button to select item to set, and using number button to set parameter. Press menu button to return. |
| --- | --- | --- | --- |
|  | IP | 192.168.001.188 |  |
|  | MASK | 255.255.255.000 |  |
|  | GW (Gateway) | 192.168.001.001 |  |
|  | MAIN Stream | 3840*2160/1920*1080 720p/1024*576 |  |
|  | BIT RATE | 10240~20480k |  |
|  | SUB Stream | 640*360 |  |
|  | BIT RATE | 10240~20480k |  |

| RESET | SYS RESET | Reset communication parameter to default |
| --- | --- | --- |
|  | CAM RESET | Reset camera parameter to default |
|  | PT RESET | Reset pan/tilt parameter to default |
|  | ALL RESET | Reset all parameter to default |

| INFO | IR ADDR | Camera IR control address |
| --- | --- | --- |
|  | USB | USB firmware version |
|  | CLIENT | Default client end protocol: VISCA |
|  | ARM VER | ARM firmware version |
|  | FPGA VER | FPGA firmware version |
|  | CAM VER | Camera version |
|  | RELEASE | Software release date |

UVC CONTROL

1. Only run the client software after the USB3.0 camera has completed self-configuration (the IR indicator in blue color and will not flash); otherwise may cause black video issue.

2. Make sure the USB3.0 camera is recognized by the PC Device Manager.

3．Make sure the interval of video format switching more than 3 seconds, otherwise black video maybe caused.

4．Make sure the interval of control command sending from the server (via USB) to the camera no less than 250ms.

5．Support standard UVC interface.

| PU_BRIGHTNESS_CONTROL | 81 01 04 4d 00 00 0p 0q FF |
| --- | --- |
| PU_CONTRAST_CONTROL | 81 01 04 A2 00 00 0p 0q FF |
| PU_SATURATION_CONTROL | 81 01 04 A1 00 00 0p 0q FF |
| PU_SHARPNESS_CONTROL | 8x 01 04 42 00 00 0p 0q FF |
| PU_GAMMA_CONTROL | 8x 01 04 5B 0p FF |
| PU_WHITE_BALANCE_TEMPERATURE_CONTROL | 8x 01 04 35 0X FF |
| PU_BACKLIGHT_COMPENSATION_CONTROL | 81 01 04 33 02/03 FF |
| PU_POWER_LINE_FREQUENCY_CONTROL | 8x 01 04 AA 00/01/02 FF |
| CT_ZOOM_ABSOLUTE_CONTROL | 8x 01 04 47 0p 0q 0r 0s FF |
| CT_PANTILT_ABSOLUTE_CONTROL | 8x 01 06 02 VV WW 0Y 0Y 0Y 0Y 0Z 0Z 0Z 0Z F |
| CT_PANTILT_RELATIVE_CONTROL | 8x 01 06 01 pp qq rr ss FF |
| CT_ZOOM_RELATIVE_CONTROL | 8x 01 04 07 pp FF |

# WEB SETTING

- Download and install Flash Player

When visit IP camera via Internet Explore browser the first time, need to install Flash Player, we suggest user download it from flash official website to get latest version:

https://www.flash.cn/english

after installation, we will be able to see bellow via PC’s Programs and Features Control Panel:

- Login

Run browser, input IP address( defaulted IP address is 192.168.1.188), to enter login interface, can select Language (Chinese or English), input admin and password to login as following:

(Default admin: admin   Default password: admin)

- Real-time Preview:

If you are log in web interface first time, there maybe show up a mistake notice as bellow, the reason is the explorer prevent the web interface to run Flash Player, what we need to do is to enter explorer setting, to set it allow to use Flash Player.

Preview interface as above image, on the right side, there are options to control camera pan, tilt, zoom, focus, presets, focus speed, zoom speed can be set. On the top of the image, main stream and sub stream preview can be selected, image width&height rate can be selected, and full size view can be selected.

- Parameter Setting

Click “Setting” to enter into parameter setting interafeace as following:

Video Encode: can set image encode mode, main stream and sub stream resolution/bit rate/frame rate, bit rate control way, and I frame interval etc as above image

Video Transmission: can set RTMP streaming, such as YouTube,Facebook application which use RTMP address, to live streaming video, can set to enable or close the streaming; also can start and close the NDI video transmission.

Image Adjust can set focus, exposure, white balance, image, image quality, noise-reduction, as following picture

Focus including focus mode, default focal distance, digital zoom etc

Exposure includes exposure mode, shutter speed, gain, iris, brightness, and anti-flicker.

White Balance includes white balance mode, red gain, blue gain.

Image includes mirror, flip, backlight compensation, Gamma, WDR(wide dynamic range).

Image Quality includes brightness, sharpness, contrast, saturation

Noise Reduction includes 2D/3D reduction. There is on/off option for 2D, and off/auto/1~4 six options.

“Ethernet” includes DHCP mode, IP address, subnet mask, default gateway, http port, web port, main stream port, sub stream port.

Default parameter as following:

| DHCP | OFF | HTTP port | 80 |
| --- | --- | --- | --- |
| IP address | 192.168.1.188 | RTSP port | 554 |
| Subnet mask | 255.255.255.0 | RTMP port | 1935 |
| Default gateway | 192.168.1.1 |  |  |

“Firmware upgrade”: it is for camera program upgrade, currently only for ISP part update. How to update:

As following picture, click “clicking to upload file” icon, open dialog box, select to open the file, and click “upgrade” to start.

DO NOT power off or do other operation when upgrading, reboot the camera after 5 min when upgrade finished.

Then login web end to select “reset all” to reset the camera completely.

Reset to default : reset the camera to default setting

Reset simply: reset camera image parameter

Reset Completelyall: reset camera Ethernet and image parameter, language and protocol will not be reset.

Reboot: Reboot ISP part of camera

Account Setting: is used for setting camera account and password

Input the account firstly, then input same password twice, click set to finish

Please remember account and password, otherwise you may be not able to login.

# VIEW RTSP VIDEO VIA VLC

Default RTSP main streaming address: rtsp://192.168.1.188/stream/main

Default RTSP sub streaming address: rtsp://192.168.1.188/stream/sub

Default RTMP main streaming address: rtmp://192.168.1.188:1935/app/rtmpstream0

Default RTMP sub streaming address:rtmp://192.168.1.188:1935/app/rtmpstream1

1, Run VLC Media Player.

2, Media->network stream, to enter into “open media” interface.

3, Input RTSP address in URL as following:

4, Click play to view the real time image.

Note: If there is much image lag, select “more option” to enter into following setting, change buffer time smaller (VLC default buffer time is 1000ms).

# NewTek Tools Guide

- Image Preview

A. Download the NewTek NDI Tools via https://ndi.tv/tools/ and install it.

B. Find out the NDI 4 Tools/Studio Monitor via Windows toolbars, and then open it, as bellow:

C. Right click on the Studio Monitor screen, select the preview device:

- Pan Tilt Control

Refer to above picture, once open the video via Studio Monitor, it will show up the control panel on the right side, to control camera pan, tilt, zoom, focus, preset, focus.

- Run WEB via Studio Monitor

Refer to above picture, once open the video via Studio Monitor, there will show up a setting icon at the lower right corner, single click this iron to enter WEB UI.

4.  How to use NDI tools to Virtual Input CAMERA

A. find out the NDI 4 Tools/Virtual Input via Windows toolbars, open it, then it will show up the NDI Virtual Input icon at the Windows toolbars, as bellow picture shows:

B. Right click on the NDI Virtual Input icon, to select the virtual device name:

C. Take Zoom for example, select NewTek NDI Video as video camera, as bellow picture shows:

This also work for other applications, such as GotoMeeting,Skype for Business, Hangouts.

# VISCA OVER IP

VISCA over IP means VISCA protocol transmit via IP, to reduce RS232/RS485 cable layout (the controller must support IP communication function)

Communication port spec:

- Control port: RJ45 Gigabit LAN

- IP protocol: IPv4

- Transmit protocol: UDP

- IP address: set via web end or OSD menu

- Port address: 52381

- Confirm send/transmission control: depend on applied program

- Applied range: in the same segment, not suitable for bridge network.

- Turn on camera: In the menu, set VISCA option to OVER IP

How to use VISCA over IP

VISCA Command

It means commands from controller to peripheral equipment, when peripheral equipment receives commands, then return ACK. When commands executed, will return complete message.

For different commands, camera will return different message.

VISCA Inquiry

It means inquiry from controller to peripheral equipment when peripheral equipment receives this kind of commands, it will return required message.

VISCA Reply

It means ACK, complete message, reply or error reply, it is sent from peripheral equipment to controller.

Command format: the following is message head and valid message format.

Note: LAN output way is big-endian, LSB is in the front.

Payload type:

Data definition as following:

| Name | Value (Byte 0) | Value (Byte 0) | Value (Byte 0) |
| --- | --- | --- | --- |
| VISCA command | 0x01 | 0x00 | Stores the VISCA command. |
| VISCA inquiry | 0x01 | 0x10 | Stores the VISCA inquiry. |
| VISCA reply | 0x01 | 0x11 | Stores the reply for the VISCA command and VISCA inquiry, or VISCA device setting command. |
| VISCA device setting command | 0x01 | 0x20 | Stores the VISCA device setting command. |
| Control command | 0x02 | 0x00 | Stores the control command. |
| Control reply | 0x02 | 0x01 | Stores the reply for the control command. |

Payload length

Valid data length in Payload (1~16), is command length.

For example, when valid data length is 16 byte

Byte 2 : 0x00    Byte 3 : 0x10

Controller will save sequence number of each command, when one command sent, the sequence number of the command will add 1, when the sequence number becomes the max value, it will change to 0 for next time. The peripheral equipment will save sequence number of each command, and return the sequence number to the controller.

Payload

According to Payload type, the following data will be saved.

- VISCA command

Save VISCA command packet

- VISCA inquiry

Save VISCA message packet

- VISCA reply

Save VISCA return packet

- VISCA device setting command

Save VISCA equipment setting command packet.

- Control command

The following data is saved in control command payload

- Controlled reply

The following data is saved in return command payload of control command.

Delivery confirmation

VISCA over IP uses UDP as transmission communication protocol, UDP communication message transmission is not stable, it is necessary to confirm delivery and resent in application.

Generally, when controller sends a command to peripheral equipment, controller will wait for the return message then send the next command, we can detect and confirm if the peripheral equipment receive the commands from return message’s lag time. If controller shows it is overtime, it is regarded as error transmission.

If controller shows it is overtime, resend the commands to check peripheral’s status, resent command sequence number is same as last command, the following chart list the received message and status after resending the commands.

Sequence chart as following

Note: Do not set IP address, subnet mask, gateway parameter in VISCA over IP command, otherwise, it will cause network breaks off. Due to change these parameter, network will be in off status.

# Text boxes

（1）     （2）     （3）

Sequence chart when returned message lost

Sequence chart when command lost